## Slide 1
Activity 1
Go internet to operate home appliances

## Slide 2: Ethernet Shield
What is an Ethernet Shield:
The Arduino Ethernet Shield allows an Arduino board to connect to the internet.
Features:
Ethernet Chip:
The shield is based on the Wiznet (W5100) ethernet chip.
Provides a network (IP) stack capable of both TCP and UDP.
Supports up to four simultaneous socket connections.
Micro SD Card:
The latest revision(v 5.0) adds a micro-SD card slot
Can be used to store files for serving over the network.
Compatible with the Arduino Duemilanove and Mega
Communication with Arduino
Arduino communicates with both the W5100 and SD card using the SPI bus (through ICSP header).
SPI consists of digital pins 11, 12, and 13 on Uno and Duemilanove and pins 50, 51, and 52 on Mega
Pin 10 is used to select the W5100 and pin 4 for the SD card (both Duemilanove and Uno) and cannot be used for general i/o.
On the Mega, SS pin-53 must be kept as an output for SPI interface to work.

## Slide 3
Note: Because the W5100 and SD card share the SPI bus, only one can be active at a time. To do this with the SD card, set pin 4 as an output and write a high to it. For the W5100, set digital pin 10 as a high output.
Ethernet Chip datasheet:
http://www.wiznet.co.kr/UpLoad_Files/ReferenceFiles/W5100_Datasheet_v1.2.2.pdf
The reset button on the shield resets both the W5100 and the Arduino board.
The shield provides a standard RJ45 ethernet jack.
The shield contains a number of informational LEDs:
  PWR/ON: indicates that the board and shield are powered
  LINK: indicates the presence of a network link and flashes when the shield transmits or receives data
  100M: indicates the presence of a 100 Mb/s network connection (as opposed to 10 Mb/s)
  RX: flashes when the shield receives data
  TX: flashes when the shield sends data

## Slide 4
Ethernet library
Allows an Arduino board to connect to the internet.
It can serve as either a server accepting incoming connections or a client making outgoing ones.
Class | Functions under each class | Use
Ethernet class - Initializes the ethernet library and network settings. | begin() localIP() maintain() | - Initializes the ethernet library and network settings. - Obtains the IP address of the Ethernet shield - Allows for the renewal of DHCP leases(given on the IP address for an amount of time)
IPAddress class - Works with local and remote IP addressing. | IPAddress() | - Defines an IP address. - It can be used to declare both local and remote addresses.
Server class -Programs running on other computers or devices - Creates servers which can send data to and receive data from connected clients | EthernetServer() begin() available() write() println() | - Create a server that listens for incoming connections on the specified port. - Tells the server to begin listening for incoming connections. - Gets a client that is connected to the server and has data available for reading. - Write data to all the clients connected to a server - Print data, followed by a new line, to all the clients connected to a server
Client class - Creates clients that can connect to servers and send and receive data. | EthernetClient() connected() connect() available() read() flush() | - Creates a client which can connect to a specified internet IP address and port - Checks whether or not the client is connected - Connects to a specified IP address and port. - Returns the number of bytes available for reading - Read the next byte received from the server connected - Discard any bytes that have been written to the client but not yet - read.

## Slide 5: Project: Home Automation
Objective: Use internet to turn on home appliances(e.g. Table lamp)
Steps:
Place the Ethernet shield on top of the Arduino board
Connect the usb cable from computer to arduino and the Ethernet cable from the router to ethernet port of the ethernet shield
Modify the example program named ‘WebServer’ (located at:
Arduino sketch->File->Examples->Ethernet->WebServer)
- Replace the IP address in the program by the newly found IP address. This will be the IP address of the Arduino Server.
- modify the program to accept user input from internet
4. Upload the File->Examples->Ethernet->DhcpAdressPrinter and click monitor to know the IP address assigned to the Arduino ‘server’
5. Make the transistor switching circuit to connect to the Arduino. Connect the VCC, Digital OUTPUT(pin2) and GND of the Arduino to proper pins of the circuit.
Pick up a table lamp and connect to the relay isolator circuit in such a way that the relay works as a switch to turn on/off the lamp
Type the IP adress on internet and click the check box to turn on/off the lamp

## Slide 6: Modify the example program
Code:
#include <SPI.h>
#include <Ethernet.h>
byte mac[] = { 0xDE, 0xAD, 0xBE, 0xEF, 0xFE, 0xED }; // MAC address from Ethernet shield sticker under board
IPAddress ip(192, 168, 1, 105); // IP address, may need to change depending on network
EthernetServer server(80); // create a server at port 80
String HTTP_req; // stores the HTTP request
boolean LED_status = 0; // state of LED, off by default
void setup()
{
Ethernet.begin(mac, ip); // initialize Ethernet device
server.begin(); // start to listen for clients
Serial.begin(9600); // for diagnostics
pinMode(2, OUTPUT); // LED on pin 2
}
void loop()
{
EthernetClient client = server.available(); // try to get client
if (client) { // got client?
boolean currentLineIsBlank = true;
while (client.connected()) {
if (client.available()) { // client data available to read
char c = client.read(); // read 1 byte (character) from client
HTTP_req += c; // save the HTTP request 1 char at a time
if (c == '\n' && currentLineIsBlank) {// last line of client request is blank and ends with \n
client.println("HTTP/1.1 200 OK"); // send a standard http response header
client.println("Content-Type: text/html");
client.println("Connection: close");
client.println();

## Slide 7
// send web page
client.println("<!DOCTYPE html>");
client.println("<html>");
client.println("<head>");
client.println("<title>Arduino LED Control</title>");
client.println("</head>");
client.println("<body>");
client.println("<h1>Project: Internet Lamp</h1>");
client.println("<p>Click to switch the table Lamp(pin2) on and off.</p>"); // Indicates the body of the Webpage
client.println("<form method=\"get\">");
ProcessCheckbox(client);
client.println("</form>");
client.println("</body>");
client.println("</html>");
Serial.print(HTTP_req);
HTTP_req = ""; // finished with request, empty string
break; }
// every line of text received from the client ends with \r\n
if (c == '\n') {
currentLineIsBlank = true; // last character on line of received text
} // starting new line with next character read
else if (c != '\r') {
currentLineIsBlank = false; // a text character was received from client
}
} // end if (client.available())
} // end while (client.connected())
delay(1); // give the web browser time to receive the data
client.stop(); // close the connection
} // end if (client)
}

## Slide 8
void ProcessCheckbox(EthernetClient cl)
{
if (HTTP_req.indexOf("Lamp=2") > -1) { // if the checkbox was clicked, toggle the LED
if (LED_status) {
LED_status = 0;}
else {
LED_status = 1;} }
if (LED_status) { // switch LED on
digitalWrite(2, HIGH);
cl.println("<input type=\"checkbox\" name=\"Lamp\" value=\"2\" \ // checkbox is checked
onclick=\"submit();\" checked>Lamp"); }
else { // switch LED off
digitalWrite(2, LOW); // checkbox is unchecked
cl.println("<input type=\"checkbox\" name=\"Lamp\" value=\"2\" \
onclick=\"submit();\">Lamp");
}
}

## Slide 9: Transistor switching circuit & Relay isolator circuit
Relay isolator ckt
Transistor switching ckt

## Slide 10: Connecting on breadboard
Full circuit
Relay circuit
Voltage regulator

## Slide 11
Activity 2
Go ad-hoc to operate home appliances

## Slide 12: Wifly Shield

## Slide 13: Load Library
Put On Wifly shield into Arduino
Connect the interface and the table lamp as the same manner of the previous project
Goto: https://github.com/sparkfun/WiFly-Shield
Copy and paste the library file into Arduino Library
Open Arduino Sketch and goto
File->examples->Wifly->tools->SpiUartTerminal
Upload to Arduino

## Slide 14: Configure
Go into command mode
Set the “wlan”parameters as follows:
SSID=ARNAB
Chan=2
ExtAnt=0
Join=4
Auth=OPEN
Mask=0x1fff
Rate=12, 24 Mb
Linkmon=0
Passphrase=0

## Slide 15
3. Set the “ip” parameters as follows:
IF=DOWN
DHCP=OFF
IP=192.168.1.150:2000
NM=255.255.255.0
GW=192.168.1.1
HOST=0.0.0.0:80
PROTO=TCP,
MTU=1460
FLAGS=0x2
BACKUP=0.0.0.0

## Slide 16: Modify existing code
Modify the existing code as follows:
#include <SPI.h>
#include <WiFly.h>
int user_key;
int led = 5;
void setup() {
Serial.begin(9600);
SpiSerial.begin();
pinMode(led, OUTPUT);
Serial.write("Please Enter 1 or 0\n");
}
void loop() {
while(SpiSerial.available() > 0) {
#if ARDUINO >= 100
user_key=SpiSerial.read();
if(user_key=='1')
{
Serial.println("Light on\n");
digitalWrite(led, HIGH);
}
else if(user_key=='0')
{
Serial.println("Light off\n");
digitalWrite(led, LOW);
}
else
{
}
#else
Serial.print(SpiSerial.read(), BYTE);
#endif
}
if(Serial.available()) { // Outgoing data
#if ARDUINO >= 100
SpiSerial.write(Serial.read());
#else
SpiSerial.print(Serial.read(), BYTE);
#endif
}
}

## Slide 17
From a wifi access connect to the same ssid:ARNAB
Set the static ip of the device according to the ip of the ad-hoc network
Open a TCP terminal
Connect to Telnet
Set the port address 2000
As the terminal opens, send 1 or 0 to turn on or off the Lamp connected to Arduino