## Slide 1
WIFLY GSX
802.11 b/g wireless LAN Modules
Current Model: RN-131C

## Slide 2
PIO4=Green LED:
ON solid :Connected over TCP
Fast blink :No IP address
Slow blink: IP address OK
PIO5=Yellow LED:
ON solid :
Fast blink :Rx/Tx data transfer
Slow blink:
PIO5=Red LED:
ON solid :
Fast blink :Not Associated
Slow blink:
OFF: Associated

## Slide 3: Entering command mode
Upon power up:
The device will be in data mode
To enter command mode:
Exactly the three characters $$$ must be sent.
The device will respond with CMD.
(This will verify that your cable and comm. settings are correct)
To exit command mode
Send “exit”<cr>.
The device will respond with “EXIT”.
Response
Most valid commands will return an “AOK” response
Invalid ones will return an “ERR” description.

## Slide 4: Communication
ASCII characters can be sent through a terminal emulator connected to the UART or via Telnet.
UART
When using the UART communications, settings should match the settings used when RN-131c connects, e.g. the default is:
9600 baudrate,
8 bits,
No Parity,
1 stop bit
hardware flow control disabled.

## Slide 5
Configuring the module to make connections is a two set process:
First, you need to associate with a access point (AP)
Second, you need to open a connection.
To configure the module over the WiFi link
The module must be associated to a network to connect to it
program the network settings.
  Configuring the module using adhoc mode:
Once in adhoc mode open up a telnet window on IP address 169.254.1.1 port 2000
  Configuring the module using the UART mode
Open a terminal emulator on the COM port associated with that deveice.
The default baud rate is 9600, 8 bits no parity.
Joining Networks and Making Connections

## Slide 6: Connect to a WiFi
Type show net to display the current network settings.
Now find all available networks with the scan command
Type join <available SSID> to associate with an access point.
If the access point is security enabled you will need to set the pass phrase prior to issuing the join command.
To set the pass phrase for WPA use the command set wlan phrase <string>. For WEP set the key using the set wlan key <num> command.

## Slide 7: Network
Infrastucture | Ad-Hoc
An access point (AP) is the common point linking all WiFi devices. | WiFi device is linked directly to every other WiFi device on the Adhoc network. There is no access point.
The access point keeps track of who’s on the local network and directs IP packets. In many cases the AP is also a router and will forward packets from the local network to other networks and the internet. | All WiFi devices on the adhoc network participate in keeping the network alive and each keeps track of the other active devices on the network by sending and receiving beacon and probe packets.
It is also very common for the AP to be running a DHCP server which tracks and assigns IP addresses. | In most cases IP addresses are assigned through Auto IP, although one of the WiFi devices can be configured as a DHCP server.

## Slide 8
set wlan join <value>
4
Create an Adhoc network, using stored SSID, IP
address and netmask. Channel MUST be set.
DHCP should be 0 (static IP) or set to Auto-IP with
this policy. (unless another Adhoc device can act as
DHCP server)
This policy is often used instead of the hardware
jumper to creat a custom Adhoc network
set wlan auth <value>
0 Open (Default)
4 WPA2-PSK
6 Adhoc, Join any Adhoc network

## Slide 9: To enable adhoc mode from software
From command mode:
set wlan join 4
set wlan ssid my_adhoc_network
set wlan chan 1
(Turn off DHCP and set the IP address and netmask so other devices know where to connect to the adhoc WiFly GSX. Since auto IP fixes the first two bytes of the IP address you want to use the netmask of 255.255.0.0 so that other device connecting to the module can be reached.)
set ip address 169.254.1.1
set ip netmask 255.255.0.0
set ip dhcp 0
(Be sure to save your configuration, then upon reboot the module will be in adhoc mode.)
To associate with an adhoc network from another WiFly device:
set wlan ssid my_adhoc_network
reboot